## Slide 1: Computer Organizational Architecture
8-bit Processor Design

## Slide 2: Data Flow Cycle
16 bit instruction is fetched from the memory.
Opcode is decoded from the instruction i.e. 1st 4 bits.
Operands are fetched accordingly.
Operation is performed ( in ALU ) according to the opcode.
Output is either stored in register for further use or sent to the user.
Next cycle of the instruction continues.
Operand Fetch
Execution
Next Instruction
Instruction Decode
Instruction Fetch

## Slide 3: Instruction Set

## Slide 4: Immediate / Branch Instruction Set [ 16-bits ]
The Opcode resides in 15th to 12th bit.
Rd is contained in 11th to 9th bit. ( destination )
Rs is contained in 8th to 6th bit. ( source )
Immediate DATA is stored in 5th to 0th bit. ( or amount shit required )
For Branching 5th to 0th bits are used as an offset.
0th
4th
3rd
2nd
1st
11th
10th
7th
9th
8th
6th
5th
15th
14th
13th
12th

## Slide 5: R type Instruction Set [ 16-bits ]
The Opcode resides in 15th to 12th bit.
R0 is contained in 11th to 9th bit. ($a0)
R1 is contained in 8th to 6th bit. ($a1)
Rd is contained in 5th to 3th bit. ($a2)
Later part is don’t care.
0th
4th
3rd
2nd
1st
11th
10th
7th
9th
8th
6th
5th
15th
14th
13th
12th

## Slide 6: J type Instruction Set [ 16-bits ]
The Opcode resides in 15th to 12th bit.
11th to 4th bit are don’t care.
JUMP address location is stored in 3rd to 0th bit.
0th
4th
3rd
2nd
1st
11th
10th
7th
9th
8th
6th
5th
15th
14th
13th
12th

## Slide 7: Opcode Decoding….
Immediate Type
  lw :- 0000
  sw :- 0001
  Addi :- 1101
  Beq :- 1010
  Bne :- 1011
Jump Type
  j :- 1100
R Type
  add :- 0010
  sub :- 0011
  comp :- 0100
  sll :- 0101
  srl :- 0110
  and :- 0111
  or :- 1000
  xor :- 1001

## Slide 8: Circuit Elements

## Slide 9
Instruction memory
This is a combinational unit - it takes just the address bus (8 bit value) as input, and gives out a 16-bit value that is the instruction to be decoded. The address is provided by the Program Counter (PC).
Control unit
The unit that actually makes the entire processor work as expected.
The input to this is the instruction word, and the output is a set of control signals that decide, for example, whether the register file is to updated, what operation is to be done by the ALU, whether memory read or write is required etc.

## Slide 10
Program Counter
It is a 8 bit register. Under normal operations, will always increment by 1 on every clock cycle, to access the next instruction. In case of a JUMP or BRANCH type of instruction, will go to the value specified by the output of the ALU or the immediate operand in the instruction.
Register file
This is a set of 8 registers, each storing an 8 bit value. There are 2 output values Ra and Rb, whose values are selected based on the instruction word, as in the instruction definitions given above.
There is one port by which data can be written into one of the registers, there is an enable signal which decides whether to update the register.

## Slide 11
Data Memory
This is a sequential / clocked unit. At any given cycle, we are either reading from it or writing to it, with the address given by the address bus. In case of a lw (load-word) or sw (store- word) instruction, the address is either immediate or the output of the ALU. The data output of the DMEM will always go into the register file, where it gets stored into a register selected by rd.
Arithmetic and Logic Unit (ALU)
The core of the processor - all the actual computations are performed here. As shown in the instruction set, operations such as addition, subtraction and logical operations are all done in this unit. Also, the output of the ALU is used as the address for certain memory related operations.

## Slide 12: Design of the Processor
8 bit architecture

## Slide 13
CONTROL
UNIT
Address /
Data
Memory
Register files
Sign
extender
Instruction memory
P.C.
ALU
MUX
MUX
MUX
MUX
Clock
Clock

## Slide 14: Design of Arithmetic and Logic Unit

## Slide 15
ADD
SUB
~
L Shift
R Shift
AND
OR
XOR
DECODER
OPCODE
OUTPUT
A
B
OR

## Slide 16: Design of Control Unit

## Slide 17
Control Unit
Program Counter’s MUX
ALU
Data Memory Read
Data Memory Write
Instruction Memory
Sign Extender MUX
MUX (Instruction Mem)
MUX (Data Mem)
C
O
N
T
R
O
L
B
U
S
Instruction
Memory
D
E
C
O
D
E
R

## Slide 18: Group 20
Nikhil Kumar Gujrati
Harsh Kochar
Aditya Kumar
Kamran Hussain
Abhinav Batta
IIT2018048
IIT2018049
IIT2018046
IIT2018036
IIT2018010
THANK YOU 